MOST USED VARIABLES (IDL INDEX CONVENTION)

index convention:
i       level index  (0:nk-1)
j       level index  (0:nk-1)   (j=upper level,  i=lower level)
ih      level index for nh array  (0:5)
kr      transition index  (0:nrad-1) where (0:nline-1) are lines, 
                                           (nline:nrad-1) are continua
krc     continuum transition index  (0:nrad-nline-1)  =kr-nline
kfx     fixed transition index  (0:nrfix-1)
k       depth index  (0:ndep-1)
mu      angle index  (0:nmu-1)
nu      frequency index (0:nq(kr)-1) or (0:nq(kr))


after running MULRD

nk               number of levels including continuum levels
nrad             number of radiative transitions treated in detail
nline            number of radiative bound-bound transitions
nrfix            number of transitions with fixed rates
nq(kr)           number of frequencies
nmu              number of angles
ndep             number of depth points

atomid           4 character identification of atom.
abnd             atomic abundance, log scale with hydrogen=12
awgt             atomic weight. input in atomic units, converted to cgs

ev(i)            energy above ground state. input in cm-1, converted to ev
g(i)             statistical weight of level
label(i)         20 character identification of level
ion(i)           ionization stage of level, 1=neutral

jrad(kr)         jrad(kr)-1 is upper level of radiative transition kr
irad(kr)         irad(kr)-1 is lower level of radiative transition kr
krad(i,j)        krad(i,j)=krad(j,i) is the number of the transition i-j
f(kr)            oscillator strength
ga(kr)           radiative damping parameter
gw(kr)           van der waals damping parameter
gq(kr)           stark damping parameter
alamb(kr)        vacuum wavelength in angstrom
ktrans(kr)       ktrans(kr) is continuum transition nr for transition kr
                  krc=ktrans(kr)

a(kr)            einstein a coefficient
b(i,j)           einstein b coefficient
c(i,j,k)         collisional transition rate

jfx(kfx)         jfx(kfx)-1 is upper level of fixed transition kfx
ifx(kfx)         ifx(kfx)-1 is lower level of fixed transition kfx
ipho(kfx)        =1 continuum, =0 line
a0(kfx)          crossection at limit
trad(kfx)        brightness temperature for continua
itrad(kfx)       radiation temperature option. =1 rad.temp=temp,
                 =2 photospheric option, rad.temp=temp out to temp.lt.trad
                    then temp=trad outwards
                 =3 chromospheric option, rad.temp=temp except when
                    temp .gt. trad and temp increasing outwards.
                    then rad.temp=trad

dnyd(k)          doppler width in units of a typical doppler width
adamp(k,kr)      voigt damping parameter


n(i,k)           population density in cm-3
nstar(i,k)       lte population density
totn(k)          total population density of atom

alfac(nu,krc)    photoionization crossection
                  in nu=0 the frequency for the edge is stored
                  in nu=1:nq(kr) the frequency points
z(k)             n(i,k) - gij*n(j,k)
gij              g(i)/g(j) for bb transitions

qnorm            unit typical doppler width in km per second at line center
hn3c2            h*ny**3/c**2

q(nu,kr)         frequency variable, in units of a typical doppler width
                  positive q for increased frequency
qmax(kr)         maximum frequency, same units as q
q0(kr)           frequency within which quadrature points are distributed
                  linearly instead of logarithmically
ind(kr)          =1 for one sided quadrature (symmetric profile)
                 =2 for two sided quadrature (asymmetric profile)
frq(nu,krc)      frequency in hz for continua
                  in nu=0 the frequency for the edge is stored
                  in nu=1:nq(kr) the frequency points

xmu(mu)          cosine of angle

atmoid           72 character identification of atmosphere used
dpid             72 character identification of depth-scale
dptype           =t  depth scale is tauscale, =m depth scale is mass scale,
                     see  routine  atmos

grav             gravitation acceleration
cmass(k)         column mass
temp(k)          temperature
nne(k)           electron density
vel(k)           macroscopic velocity in doppler units
vturb(k)         microturbulence velocity in doppler units
height(k)        height above tau5000=1 in kilometers

bh(ih,k)         departure coefficient for hydrogen
nh(ih,k)         population density for hydrogen
rho(k)           density

tau(k)           standard optical depth
taulg(k)         alog10(tau)
xnorm(k)         standard opacity in cm**2 per cm**3
sl(k,kr)         line source function
bp(k,kr)         planck function

dlgtmx(k)        maximum delta lg tauq for each depth

rij(k,kr)        radiative rate from i to j per ni atom
rji(k,kr)        radiative rate from j to i per nj atom

flux(nu,kr)      monochromatic physical flux in cgs units
outint(nu,mu,kr) monochromatic surface intensity in cgs units
                  in nu=0 the continuum intensity is stored
                  in nu=1:nq(kr) outint for the nu-points of the transition

cool(k,kr)       cooling function in erg/cm**3/s
weq(kr)          equivalent width
weqlte(kr)       equivalent width in lte


physical constants:

ee               electron charge
em               electron mass
hh               planck constant
cc               velocity of light
bk               boltzmann constant
uu               universal mass constant
hce              hh*cc/ee*1.e8    lambda(angstrom)=hce/energy(ev)
hc2              2*hh*cc*1.e24    2*h*ny**3/c**2=hc2/lambda(angstrom)**3
hck              hh*cc/bk*1.e8    h*ny/kt=hck/lambda(angstrom)/t
ek               ee/bk
pi               pi





after running NYRD,kr,nu

tauq(k)          monochromatic optical depth
s(k)             monochromatic source function
sbck(k)          background source function, including scattering term
xcont(k)         background opacity relative to standard opacity
x(k)             total opacity relative to standard opacity
iplus(k)         i+
iminus(k)        i-
jny(k)           mean intensity

p(k)             feautrier mean intensity
pms(k)           p - s
rny(k)           xcont/x
scat(k)          scattering relative to background opacity
sc(k)            background source function, excluding scattering term




after running CNTRB:

cntrbi(k,nu,kr)  contribution function to intensity on a alog10(tau) scale
cntrbr(k,nu,kr)  contribution function to relative absorption
cntrbf(k,nu,kr)  contribution function to flux 
xmeani(nu,kr)    average height of formation for intensity
xmeanr(nu,kr)    average height of formation for relative absorption
xmeanf(nu,kr)    average height of formation for flux




after running RATES:

pt(i,j,k)        total rate from level i to level j.
pt(j,i,k)        total rate from level j to level i.
pn(i,j,k)        net rate, positive=up
pn(j,i,k)        relative net rate